## Slide 1
Craig Johnson, AAØZZ
The ZZRX-40
Direct Conversion Receiver
for 40 Meters
August 18, 2016

## Slide 2
ZZRX-40
Theory of Operation
AAØZZ
August 18, 2016

## Slide 3: ZZRX-40 Theory of Operation (Direct Conversion Receiver)
Audio
Amp
Antenna
Local
Oscillator
Essential elements of ANY receiver
Speaker
Mixer
AAØZZ
August 18, 2016

## Slide 4: ZZRX-40 Theory of Operation
Audio
Amp
Antenna
Local
Oscillator
Speaker
Mixer
10 Hz
8 Hz
18 Hz and 2 Hz
Louder
Sum and difference
Incoming signal
Simple Mixing and “Direct Conversion” to audio
AAØZZ
August 18, 2016

## Slide 5: ZZRX-40 Theory of Operation
Antenna
Local
Oscillator
Speaker
Mixer
1 MHz
1 MHz
2 MHz and 0 MHz
0 Hz (just noise)
Audio
Amp
(and filter)
Sum and difference
Incoming signal
Low Pass Filter
(300 kHz max)
Simple Mixing and “Direct Conversion” to audio
AAØZZ
August 18, 2016

## Slide 6: ZZRX-40 Theory of Operation
Antenna
Local
Oscillator
Speaker
Mixer
1,000,000 Hz
1,000,600 Hz
2,000,600 Hz and 600 Hz
Louder 600 Hz
Audio
Amp
(and filter)
Sum and difference
Incoming signal
Low Pass Filter
(300 kHz max)
Also NOISE!
Simple Mixing and “Direct Conversion” to audio
AAØZZ
August 18, 2016

## Slide 7: ZZRX-40 Theory of Operation
Audio
Amp
(and filter)
Antenna
Local
Oscillator
All
Frequencies
Louder Audio
Sum and difference
One Frequency
Mixer
Add input filter
(select signal from smaller range of frequencies)
Many signals
Low Pass Filter
(300 kHz max)
Bandpass
6.5 – 7.5 MHz
Filter
AAØZZ
August 18, 2016

## Slide 8: ZZRX-40 Theory of Operation
Antenna
Local
Oscillator
Filter
All
Frequencies
Louder
Audio
One Frequency
Audio
Amp
7,040,000 Hz
14,080,000 Hz and 0 Hz
(noise)
Speaker
Mixer
(noise)
LO Zero BEAT with incoming signal
7,040,000
Sum and Difference
14,080,000
Low Pass Filter
(300 kHz max)
Removed by audio amp as low pass filter
Bandpass
6.5 – 7.5 MHz
Many signals including a
CW signal at
7,040,000 Hz
AAØZZ
August 18, 2016
(Plus others!)

## Slide 9: ZZRX-40 Theory of Operation
Antenna
Local
Oscillator
Filter
All
Frequencies
Louder
Audio
One Frequency
Audio
Amp
7,040,600 Hz
(noise)
Speaker
Mixer
600 Hz
Example 5: LO Plus 600 Hz
Low Pass Filter
(300 kHz max)
7,040,000
Sum and Difference
14,080,600 Hz
7,040,600
14,080,600 Hz and 600 Hz
600
Removed by audio amp as low pass filter
Bandpass
6.5 – 7.5 MHz
Many signals including a
CW signal at
7,040,000 Hz
AAØZZ
August 18, 2016
(Plus others!)

## Slide 10: ZZRX-40 Theory of Operation
Antenna
Local
Oscillator
Filter
All
Frequencies
Louder
Audio
One Frequency
Audio
Amp
14,079,400 Hz and 600 Hz
600 Hz
(noise)
Speaker
Mixer
7,039,400 Hz
Example 6: LO Minus 600 Hz
7,040,000
7,039,400
Sum and Difference
14,079,400 Hz
Low Pass Filter
(300 kHz max)
600
Removed by audio amp as low pass filter
Bandpass
6.5 – 7.5 MHz
Many signals including a
CW signal at
7,040,000 Hz
AAØZZ
August 18, 2016
(Plus others!)

## Slide 11: ZZRX-40 Theory of Operation
Antenna
Local
Oscillator
Filter
All
Frequencies
Louder
Audio
+ and -
Sine wave at
Audio
Audio
Amp
600 Hz
14,080,600 Hz
and
600 Hz
600 Hz
(noise)
Speaker
Mixer
(optional)
7,040,600 Hz
Better
Audio Filter
Example x: LO Plus 600Hz with Audio Filter
7,040,000
7,040,600
Removed by improved audio filter
14,080,600 Hz
600
Bandpass
6.5 – 7.5 MHz
Many signals including a
CW signal at
7,040,000 Hz
AAØZZ
August 18, 2016

## Slide 12: ZZRX-40 Theory of Operation
Audio
Amp
Antenna
Local
Oscillator
Speaker
Mixer
Bandpass
Filter
Gain
Control
Front End
AAØZZ
August 18, 2016

## Slide 13: ZZRX-40 Theory of Operation
LM386
Antenna
Local
Oscillator
Speaker
NE602
Gain
Control
Filter
And
Impedance
Transform
Front End
AAØZZ
August 18, 2016

## Slide 14: ZZRX-40 Theory of Operation
LM386
Antenna
Local
Oscillator
Speaker
NE602
~50 ohms
(NE602 input impedance)
1500 ohms
Front End
AAØZZ
August 18, 2016

## Slide 15: ZZRX-40 Theory of Operation
LM386
Antenna
Local
Oscillator
Speaker
NE602
Blocks DC
“Short” to RF
.1uF
~50 ohms
(NE602 input impedance)
1500 ohms
Front End
R1
10k
Gain
Control
AAØZZ
August 18, 2016

## Slide 16: ZZRX-40 Theory of Operation
LM386
Antenna
Local
Oscillator
Speaker
NE602
Blocks DC
“Short” to RF
.1uF
~50 ohms
(NE602 input impedance)
1500 ohms
Resonant “tank” circuit provides
bandpass filter
Xc = X(c1 in series with c2)
At resonant frequency Xc = XL
Ideal resonance at 1 frequency
but actually it’s a curve.
Split capacitors and coil provide impedance transformation
C1
C2
L1
Front End
2
1
R1
10k
180p
820p
3.3u
Gain
Control
AAØZZ
August 18, 2016

## Slide 17: ZZRX-40 Theory of Operation
LM386
Antenna
Local
Oscillator
Speaker
NE602
Blocks DC
“Short” to RF
.1uF
~50 ohms
Resonant “tank” circuit provides
bandpass filter
Xc = X(c1 in series with c2)
At resonant frequency Xc = XL
Ideal resonance at 1 frequency
but actually it’s a curve.
Split capacitors and coil provide impedance transformation
C1
C2
L1
Front End
2
1
1500 ohms
+6v
8
3
R1
10k
180p
820p
3.3u
Gain
Control
AAØZZ
August 18, 2016

## Slide 18: ZZRX-40 Theory of Operation
Antenna
Local
Oscillator
Filter
All
Frequencies
Louder
Audio
One Frequency
Audio
Amp
7,040,600 Hz
(noise)
Speaker
Mixer
600 Hz
LO Plus 600 Hz
Low Pass Filter
(300 kHz max)
7,040,000
Sum and Difference
14,080,600 Hz
7,040,600
14,080,600 Hz and 600 Hz
600
Removed by audio amp as low pass filter
Bandpass
6.5 – 7.5 MHz
Many signals including a
CW signal at
7,040,000 Hz
REVIEW
AAØZZ
August 18, 2016

## Slide 19: ZZRX-40 Theory of Operation
Antenna
Local
Oscillator
Filter
All
Frequencies
Louder
Audio
One Frequency
Audio
Amp
7,039,400 Hz
(noise)
Speaker
Mixer
600 Hz
LO Minus 600 Hz
Low Pass Filter
(300 kHz max)
7,040,000
Sum and Difference
14,079,400 Hz
7,039,400
14,079,400 Hz and 600 Hz
600
Removed by audio amp as low pass filter
Bandpass
6.5 – 7.5 MHz
Many signals including a
CW signal at
7,040,000 Hz
REVIEW
AAØZZ
August 18, 2016

## Slide 20: ZZRX-40 Theory of Operation
LM386
Antenna
Local
Oscillator
Speaker
NE602
.1uF
~50 ohms
C1
C2
L1
Audio Out
2
1
4
5
1500 ohms
RF
2
3
+6v
8
3
R1
10k
180p
820p
3.3u
Gain
Control
5
AAØZZ
August 18, 2016

## Slide 21: ZZRX-40 Theory of Operation
LM386
Antenna
Local
Oscillator
Speaker
NE602
.1uF
~50 ohms
C1
C2
L1
Audio Out
2
1
4
5
1500 ohms
RF
2
3
+6v
8
3
R1
10k
180p
820p
3.3u
Gain
Control
5
AUDIO
AAØZZ
August 18, 2016

## Slide 22: ZZRX-40 Theory of Operation
LM386
Antenna
Local
Oscillator
Speaker
NE602
.1uF
~50 ohms
C1
C2
L1
Audio Out
2
1
4
5
1500 ohms
C8
0.1u
DC Block
DC Block
2
3
+6v
8
3
Audio Pass
Audio Pass
R1
10k
180p
820p
3.3u
Gain
Control
5
AAØZZ
August 18, 2016

## Slide 23: ZZRX-40 Theory of Operation
LM386
Antenna
Local
Oscillator
Speaker
NE602
.1uF
~50 ohms
C1
C2
L1
Audio Out
2
1
4
5
1500 ohms
C8
0.1u
C9
C10
0.22u
0.22u
2
3
DC Bias
DC Bias
+6v
8
3
R1
10k
180p
820p
3.3u
Gain
Control
5
AAØZZ
August 18, 2016

## Slide 24: ZZRX-40 Theory of Operation
LM386
Antenna
Local
Oscillator
Speaker
NE602
.1uF
~50 ohms
C1
C2
L1
Audio Out
2
1
4
5
1500 ohms
C8
0.1u
C9
C10
0.22u
0.22u
2
3
R7
R6
10k
10k
+6v
8
3
R1
10k
180p
820p
3.3u
Gain
Control
5
AAØZZ
August 18, 2016

## Slide 25: ZZRX-40 Theory of Operation
LM386
Antenna
Local
Oscillator
Speaker
NE602
.1uF
~50 ohms
C1
C2
L1
Audio Out
2
1
4
5
1500 ohms
C8
0.1u
C9
C10
0.22u
0.22u
2
3
R7
R6
10k
10k
+6v
8
3
+6v
6
4
R1
10k
180p
820p
3.3u
Gain
Control
5
AAØZZ
August 18, 2016

## Slide 26: ZZRX-40 Theory of Operation
LM386
Antenna
Local
Oscillator
Speaker
NE602
.1uF
~50 ohms
C1
C2
L1
Audio Out
2
1
4
5
1500 ohms
C8
0.1u
C9
C10
0.22u
0.22u
2
3
R7
R6
10k
10k
Gain select
1
8
=200
+6v
8
3
+6v
6
4
R1
10k
180p
820p
3.3u
Gain
Control
5
AAØZZ
August 18, 2016

## Slide 27: ZZRX-40 Theory of Operation
LM386
Antenna
Local
Oscillator
Speaker
NE602
.1uF
~50 ohms
C1
C2
L1
Audio Out
2
1
4
5
1500 ohms
C8
0.1u
C9
C10
0.22u
0.22u
2
3
R7
R6
10k
10k
1
8
4.7u
C11
+
+6v
8
3
+6v
6
4
R1
10k
180p
820p
3.3u
Gain
Control
5
AAØZZ
August 18, 2016

## Slide 28: ZZRX-40 Theory of Operation
LM386
Antenna
Local
Oscillator
Speaker
NE602
.1uF
~50 ohms
C1
C2
L1
Audio Out
2
1
4
5
1500 ohms
C8
0.1u
C9
C10
0.22u
0.22u
2
3
R7
R6
10k
10k
1
8
4.7u
C11
+
+
7
Bypass
+6v
8
3
+6v
6
4
R1
10k
180p
820p
3.3u
Gain
Control
5
AAØZZ
August 18, 2016

## Slide 29: ZZRX-40 Theory of Operation
LM386
Antenna
Local
Oscillator
Speaker
NE602
.1uF
~50 ohms
C1
C2
L1
Audio Out
2
1
4
5
1500 ohms
C8
0.1u
C9
C10
0.22u
0.22u
2
3
R7
R6
10k
10k
1
8
4.7u
C11
+
+
7
2.2u
C12
3
+6v
8
+6v
6
4
R1
10k
180p
820p
3.3u
Gain
Control
5
AAØZZ
August 18, 2016

## Slide 30: ZZRX-40 Theory of Operation
LM386
Antenna
Local
Oscillator
Speaker
NE602
.1uF
~50 ohms
C1
C2
L1
Audio Out
2
1
4
5
1500 ohms
C8
0.1u
C9
C10
0.22u
0.22u
2
3
R7
R6
10k
10k
1
8
4.7u
C11
+
+
7
2.2u
C12
3
+6v
8
+6v
6
4
DC Block
Audio Pass
R1
10k
180p
820p
3.3u
Gain
Control
5
AAØZZ
August 18, 2016

## Slide 31: ZZRX-40 Theory of Operation
LM386
Antenna
Local
Oscillator
Speaker
NE602
.1uF
~50 ohms
C1
C2
L1
Audio Out
2
1
4
5
1500 ohms
C8
0.1u
C9
C10
0.22u
0.22u
2
3
R7
R6
10k
10k
1
8
4.7u
C11
+
+
7
2.2u
C12
3
+6v
8
+6v
6
4
+
100u
C15
Bypass
Noise
R1
10k
180p
820p
3.3u
Gain
Control
5
AAØZZ
August 18, 2016

## Slide 32: ZZRX-40 Theory of Operation
LM386
Antenna
Local
Oscillator
Speaker
NE602
.1uF
~50 ohms
C1
C2
L1
Audio Out
2
1
4
5
1500 ohms
C8
0.1u
C9
C10
0.22u
0.22u
2
3
R7
R6
10k
10k
1
8
4.7u
C11
+
+
7
2.2u
C12
3
+6v
8
+6v
6
4
+
100u
C15
C15
0.1u
R10
10
R1
10k
180p
820p
3.3u
Gain
Control
5
AAØZZ
August 18, 2016

## Slide 33: ZZRX-40 Theory of Operation
Out
+6–8v
Simple Crystal Oscillator
AAØZZ
August 18, 2016

## Slide 34: ZZRX-40 Theory of Operation
Out
+6–8v
Simple Crystal Oscillator – alternate biasing
AAØZZ
August 18, 2016

## Slide 35: ZZRX-40 Theory of Operation
7
6
8
3
+6–8v
Simple Crystal Oscillator as LO for NE602
NE602
AAØZZ
August 18, 2016

## Slide 36: ZZRX-40 Theory of Operation
7
6
8
3
+6–8v
XTAL
100p
100p
C4
C5
NE602
Simple Crystal Oscillator as LO for NE602
AAØZZ
August 18, 2016

## Slide 37: ZZRX-40 Theory of Operation
LM386
Antenna
Speaker
NE602
.1uF
~50 ohms
C1
C2
L1
Crystal-controlled Local Oscillator
2
1
4
5
1500 ohms
C8
0.1u
C9
C10
0.22u
0.22u
2
3
R7
R6
10k
10k
1
8
4.7u
C11
+
+
7
2.2u
C12
3
+6v
8
+6v
6
4
+
100u
C15
C15
R10
10
C4
C5
xtal
This Local Oscillator would work for
a single frequency
6
7
R1
10k
180p
820p
3.3u
Gain
Control
0.1u
5
AAØZZ
August 18, 2016

## Slide 38: ZZRX-40 Theory of Operation
LM386
Antenna
Speaker
NE602
.1uF
~50 ohms
C1
C2
L1
2
1
4
5
1500 ohms
C8
0.1u
C9
C10
0.22u
0.22u
2
3
R7
R6
10k
10k
1
8
4.7u
C11
+
+
7
2.2u
C12
3
+6v
8
+6v
6
4
+
100u
C15
C15
R10
10
C4
C5
xtal
6
7
Inductor will pull
Crystal frequency
by a fixed amount
R1
10k
180p
820p
3.3u
Crystal-controlled Local Oscillator
0.1u
5
AAØZZ
August 18, 2016

## Slide 39: ZZRX-40 Theory of Operation
LM386
Antenna
Speaker
NE602
.1uF
~50 ohms
C1
C2
L1
2
1
4
5
1500 ohms
C8
0.1u
C9
C10
0.22u
0.22u
2
3
R7
R6
10k
10k
1
8
4.7u
C11
+
+
7
2.2u
C12
3
+6v
8
+6v
6
4
+
100u
C15
C15
R10
10
C4
C5
Variable capacitor
will pull frequency
by varying amount
6
7
R1
10k
180p
820p
3.3u
Crystal-controlled Local Oscillator
0.1u
5
xtal
AAØZZ
August 18, 2016

## Slide 40: ZZRX-40 Theory of Operation
LM386
Antenna
Speaker
NE602
.1uF
~50 ohms
C1
C2
L1
2
1
4
5
1500 ohms
C8
0.1u
C9
C10
0.22u
0.22u
2
3
R7
R6
10k
10k
1
8
4.7u
C11
+
+
7
2.2u
C12
3
+6v
8
+6v
6
4
+
100u
C15
C15
R10
10
C4
C5
Pulling the
Crystal frequency
6
7
R1
10k
820p
3.3u
180p
Crystal-controlled Local Oscillator
Gain
Control
0.1u
5
xtal
AAØZZ
August 18, 2016

## Slide 41: ZZRX-40 Theory of Operation
LM386
Antenna
Speaker
NE602
.1uF
~50 ohms
C1
C2
L1
2
1
4
5
1500 ohms
C8
0.1u
C9
C10
0.22u
0.22u
2
3
R7
R6
10k
10k
1
8
4.7u
C11
+
+
7
2.2u
C12
3
+6v
8
+6v
6
4
+
100u
C15
C15
R10
10
C4
C5
Pulling the
Crystal frequency
6
7
0 - 6v
Varactor as a
“variable capacitor”
(capacitance varies with voltage )
R1
10k
180p
820p
3.3u
Crystal-controlled Local Oscillator
0.1u
5
xtal
AAØZZ
August 18, 2016

## Slide 42: ZZRX-40 Theory of Operation
LM386
Antenna
Speaker
NE602
.1uF
~50 ohms
C1
C2
L1
2
1
4
5
1500 ohms
C8
0.1u
C9
C10
0.22u
0.22u
2
3
R7
R6
10k
10k
1
8
4.7u
C11
+
+
7
2.2u
C12
3
+6v
8
+6v
6
4
+
100u
C15
C15
R10
10
C4
C5
6
7
0 - 6v
+6v
Isolation
Pick off
0 - 6v
R1
10k
180p
820p
3.3u
Crystal-controlled Local Oscillator
0.1u
5
xtal
AAØZZ
August 18, 2016

## Slide 43: ZZRX-40 Theory of Operation
LM386
Antenna
Speaker
NE602
.1uF
~50 ohms
C1
C2
L1
2
1
4
5
1500 ohms
C8
0.1u
C9
C10
0.22u
0.22u
2
3
R7
R6
10k
10k
1
8
4.7u
C11
+
+
7
2.2u
C12
3
+6v
8
+6v
6
4
+
100u
C15
C15
R10
10
C4
C5
6
7
0 - 6v
+6v
100k
Rx
D2
L2
15uH
1N4004
R2
10k
R1
10k
180p
820p
3.3u
Crystal-controlled Local Oscillator
1N4004:
~40pF at 0.1v
~13pf at 6v
0.1u
5
xtal
AAØZZ
August 18, 2016

## Slide 44: ZZRX-40 Theory of Operation
LM386
Antenna
Speaker
NE602
.1uF
~50 ohms
C1
C2
L1
Variable Frequency Oscillator as LO
2
1
4
5
1500 ohms
C8
0.1u
C9
C10
0.22u
0.22u
2
3
R7
R6
10k
10k
1
8
4.7u
C11
+
+
7
2.2u
C12
3
+6v
8
+6v
6
4
+
100u
C15
C15
R10
10
C4
C5
6
7
0- 6v
D2
1N4004
R1
10k
180p
820p
3.3u
100k
R5
C19
100p
100p
C20
L3
4.7u
Gain
Control
0.1u
5
+6v
R2
10k
100p
100p
AAØZZ
August 18, 2016

## Slide 45: ZZRX-40 Theory of Operation
LM386
Antenna
Speaker
NE602
.1uF
~50 ohms
C1
C2
L1
Variable Frequency Oscillator as LO
2
1
4
5
1500 ohms
C8
0.1u
C9
C10
0.22u
0.22u
2
3
R7
R6
10k
10k
1
8
4.7u
C11
+
+
7
2.2u
C12
3
+6v
8
+6v
6
4
+
100u
C15
C15
R10
10
C4
C5
6
7
D2
1N4004
R1
10k
180p
820p
3.3u
100k
R5
C19
100p
100p
C20
L2
4.7u
Gain
Control
0.1u
5
+6v
R2
10k
0- 6v
100p
100p
C21
0-50pF
Set lower
band edge
AAØZZ
August 18, 2016

## Slide 46: ZZRX-40 Theory of Operation
LM386
Antenna
Speaker
NE602
.1uF
~50 ohms
C1
C2
L1
That’s it!
2
1
4
5
1500 ohms
C8
0.1u
C9
C10
0.22u
0.22u
2
3
R7
R6
10k
10k
1
8
4.7u
C11
+
+
7
2.2u
C12
3
+6v
8
+6v
6
4
+
100u
C15
C15
R10
10
C4
C5
6
7
D2
1N4004
R1
10k
180p
820p
3.3u
100k
R5
C19
100p
100p
C20
L2
4.7u
Gain
Control
0.1u
5
+6v
R2
10k
0- 6v
100p
100p
C21
0-50pF
Set lower
band edge
AAØZZ
August 18, 2016

## Slide 47
ZZRX-40
Building the
AAØZZ
August 18, 2016

## Slide 48
AAØZZ
August 18, 2016

## Slide 49
AAØZZ
August 18, 2016

## Slide 50
AAØZZ
August 18, 2016

## Slide 51
AAØZZ
August 18, 2016

## Slide 52
AAØZZ
August 18, 2016

## Slide 53
AAØZZ
August 18, 2016

## Slide 54
AAØZZ
August 18, 2016

## Slide 55
AAØZZ
August 18, 2016

## Slide 56
AAØZZ
August 18, 2016

## Slide 57
AAØZZ
August 18, 2016

## Slide 58
AAØZZ
August 18, 2016

## Slide 59
AAØZZ
August 18, 2016

## Slide 60
AAØZZ
August 18, 2016

## Slide 61
AAØZZ
August 18, 2016

## Slide 62
AAØZZ
August 18, 2016

## Slide 63
AAØZZ
August 18, 2016

## Slide 64
AA0ZZ References
Email: aa0zz@aa0zz.com
Web page: www.aa0zz.com
YAHOO Group – DDS-VFO (www.groups.yahoo.com/group/DDS-VFO)
ZZRX-40 kit availability:
4SQRP: www.4sqrp.com
YAHOO Group – PIC-EL (www.groups.yahoo.com/group/PIC-EL)
YAHOO Group – PPLL-VFO (www.groups.yahoo.com/group/PPLL-VFO)
$45 + postage
AAØZZ
August 18, 2016
YAHOO Group – ZZRX-40 (www.groups.yahoo.com/group/ZZRX-40)

## Slide 65
Questions?
AAØZZ
August 18, 2016
Demo